## Slide 1
LNP Manufacturing and Process
Simulation
CL 299 presentation 4
Supervisor:
Prof. Kaustubh S. Rane Department of Chemical Engineering
Presented by:
Rhythem Soni 24110296 Aman Bola 24110032 Saket Jonwal 24110311

## Slide 2: Key Process Parameters
Parameter | Value
Flow rate ratio (aqueous : organic) | 3 : 1
Total mixer flow | 12 mL/min
Ethanol fraction after mixing | 25 %
Parameter | Value
Dilution buffer flow | 36 mL/min
Total flow after dilution | 48 mL/min
Ethanol concentration | 6.25 %
Mixer Conditions
Dilution Step

## Slide 3
Parameter | Value
Membrane MWCO | 100 kDa
TMP | 1 bar
Crossflow rate | 30–100 mL/min
Concentration factor | 6×
TFF Operation

## Slide 4: Material Balance Key Streams
Stream | Flow
Organic lipid solution | 3 mL/min
Aqueous mRNA solution | 9 mL/min
Dilution buffer | 36 mL/min
Feed Streams
Total Feed to TFF: 48 mL/min
Final Product Flow Rate: 7.5 mL/min
Composition:
Lipids = 30 mg/min
mRNA = 4.5 mg/min
Buffer salts = 102 mg/min
Overall Balance: Input = 48 mL/min
Output = 48 mL/min

## Slide 5: The Nanoparticle Structure (Primary Lipids)
Ionizable Lipids
Definition: Lipids that change their electrical charge based on the surrounding pH (acidic vs. neutral).
Use: Bind and encapsulate the negatively charged RNA payload, and later help release it inside the target cell.
Helper Phospholipids
Definition: Structural lipids that form the foundation of standard cell membranes.
Use: Provide structural integrity to the LNP and help the nanoparticle fuse with the target cell's membrane.

## Slide 6
Sterols
Definition: Rigid, ring-structured lipid molecules (e.g., cholesterol).
Use: Fill gaps between other lipids to regulate the structural fluidity and stability of the nanoparticle core.
PEG Lipids
Definition: Lipids attached to polyethylene glycol (PEG) polymer chains.
Use: Coat the LNP surface to prevent particles from clumping together and hide them from the immune system.

## Slide 7: Manufacturing & Processing Agents
Organic Solvents
Definition: Carbon-based liquids (e.g., ethanol, methanol) capable of dissolving hydrophobic materials.
Use: Dissolve the lipids so they can be mixed with the water-soluble RNA during the initial nanoparticle formation process.
Buffer Acids & Salts
Definition: Chemical systems designed to maintain a specific, constant pH in a solution.
Use: Control the pH during mixing to ensure ionizable lipids carry the necessary positive charge to efficiently bind the RNA.

## Slide 8: Storage & Protection Excipients
Cryoprotectants
Definition: Specific sugars or polyols (e.g., sucrose, trehalose) that protect physical structures at freezing temperatures.
Use: Prevent ice crystals from physically piercing and destroying the fragile lipid spheres during deep-freeze storage.
Antioxidants
Definition: Compounds that inhibit oxidation reactions.
Use: Protect lipids and RNA from oxidative degradation, extending the overall shelf life of the formulation.

## Slide 9
Chelating Agents
Definition: Molecules (e.g., EDTA) that bind tightly to free, reactive metal ions.
Use: Trap trace metals that would otherwise catalyze drug degradation or activate enzymes that destroy RNA.

## Slide 10: Final Formulation & Delivery Excipients
Surfactants
Definition: Surface-active agents (e.g., Polysorbate 20) that lower the surface tension of liquids.
Use: Prevent the nanoparticles from sticking to the walls of glass vials, syringes, and manufacturing tubing.
Salts
Definition: Standard ionic compounds (e.g., Sodium Chloride).
Use: Ensure the final liquid suspension matches the salt concentration of human blood to prevent cell damage and pain upon injection.

## Slide 11
Stabilizers
Definition: Viscosity-modifying or structure-supporting agents (e.g., Glycerol).
Use: Keep the nanoparticle suspension evenly mixed and prevent the particles from settling or aggregating over time.

## Slide 12
Level | Sample removal | Real-time | Control capability
Offline | Yes | No | Low
At-line | Yes | Limited | Medium
Online | Automated | Near real-time | High
Inline | No | Real-time | Highest

## Slide 13: INLINE
Near-infrared Spectroscopy (NIR) this technique measure molecular vibrations a fiber-optic NIR probe is installed directly inside the tablet coating equipment, measuring spectra continuously during coating.
Infrared Spectroscopy used to identify chemical bonding For bioreactors.
Nuclear Magnetic resonance (NMR) used to determine molecular structuresflow water-proton NMR can be used as an inline PAT tool in continuous biomanufacturing to monitor protein concentration and aggregation in real time using water-proton relaxation signals.
Raman Spectroscopy analyse molecular structure and composition by measuring light scattering from molecules.  powder blending process
Dynamic Light Scattering (DLS) used to measure particle size.
Reflective Interference Spectroscopy measures interference patterns of reflected light to detect changes in surface thickness or refractive index and used as an optical biosensor to detect biomolecular binding by measuring changes in the interference of reflected light from a sensor surface

## Slide 14
Surface Plasmon resonance (SPR) Surface plasmon resonance is an optical sensing technique that measures changes in refractive index at a metal surface to detect molecular interaction
Mass Spectroscopy provides information about the molecular weight to monitor and characterize monoclonal antibodies in real time during purification.
NIR Turbidity uses Near-Infrared (NIR) light to determine how cloudy or particle-rich a liquid is.
IR Absorption Infrared (IR) absorption occurs when molecules absorb infrared radiation, causing changes in vibrational and rotational energy levels.
Zeta potential Analysis This technique determines the surface charge
PVM (Particle Vision and Measurement) captures real-time images of particles inside a process to monitor particle shape, size, and behavior.

## Slide 15
Now in addition to all the techniques using inline classification, we have some tools that are used to measure some parameters-
1. pH sensors 2. Flow meters 3. Temperature probs 4. Conductivity sensors

## Slide 16: ONLINE
NIR  online NIR spectroscopy with an adaptive model-updating strategy to monitor industrial processes in real time as a PAT tool.
Infrared Spectroscopy & Mass Spectroscopy methanol electro-oxidation on a Pt catalyst using in-situ IR spectroscopy and online mass spectrometry to monitor reaction intermediates and products during the reaction.
NMR flow-NMR as an online PAT tool to monitor chemical reactions in real time by measuring reactant and product concentrations directly in the flowing reaction mixture.
Raman Spectroscopy
IR absorptionIR absorption at 5.85 μm to detect oxidation in lubricating oil and proposes a compact sensor for online oil condition monitoring.
High-Performance Liquid Chromatography (HPLC) On-line possible via auto-samplers for drug loading, encapsulation efficiency, or degradation monitoring.

## Slide 17
Fourier Transform Infrared Spectroscopy (FTIR) online FT-IR spectroscopy as a PAT tool to monitor glucose consumption and ethanol production in yeast fermentation in real time.
Photometric stereo imaging Photometric stereo imaging reconstructs surface shape by analyzing images taken under different lighting angles.

## Slide 18: ATLINE
Zeta potential analysis
Fluorescence Atomic fluorescence spectrometry is a specific type of fluorescence technique used to detect trace metals by measuring fluorescence from atoms.
NIR  During fermentation, samples were taken from the bioreactor and analyzed using Near-Infrared Spectroscopy (NIR) to estimate glucose and biomass using PLS models.
Liquid Chromatography  at-line RP-UPLC (liquid chromatography) to monitor protein concentration during microfiltration.
Raman Spectroscopy  portable Raman spectroscopy used as an at-line PAT tool to characterize carbon nanomaterials and monitor their structural quality during manufacturing.

## Slide 19: OFFLINE
NMR , FTIR
Fluorescence
(Bio)chemical Analysers used to measure chemical or biological components
Confocal Spectroscopy (CICS) used for high-resolution nanoparticle characterization. offline.
Consistent cryo-electron microscopy (Cryo-EM) This technique is used to visualize nanoparticle structure and morphology at very high resolution. offline

## Slide 20
Small-angle X-ray scattering (SAXS) This technique is used to analyze nanoscale structure and internal organization of particles using X-ray scattering. offline
Optical Microscopy and Electron Microscopy helping to identify any issues like agglomeration or structural defects. Offline.
Differential Scanning Calorimetry (DSC) (Thermal analysis, not real-time). Offline.
X-ray Diffraction (XRD) This technique is used to determine crystal structure and phase composition by analyzing X-ray diffraction patterns. Offline.
NIR & Raman Spectroscopy off-line NIR was used to correlate ribbon density with chemical absorption spectra, while off-line Raman spectroscopy was used to predict tablet hardness by analyzing surface smoothness and density.

## Slide 21: Classification of techniques
Techniques | Offline | Atline | Online | Inline
Near-infrared Spectroscopy (NIR) | ✓ | ✓ | ✓ | ✓
Infrared spectroscopy |  |  | ✓ | ✓
Nuclear magnetic resonance (NMR) | ✓ |  | ✓ | ✓
Raman spectroscopy | ✓ | ✓ | ✓ | ✓
Dynamic light scattering (DLS) |  |  |  | ✓
Fluorescence | ✓ | ✓ |  | 
Surface plasmon resonance (SPR) |  |  |  | ✓

## Slide 22
Techniques | Offline | Atline | Online | Inline
Reflective Interference Spectroscopy |  |  |  | ✓
Mass spectrometry (MS) |  |  | ✓ | ✓
NIR Turbidity |  |  |  | ✓
IR Absorption |  |  | ✓ | ✓
Consistent cryo-electron microscopy (Cryo-EM) | ✓ |  |  | 
Confocal Spectroscopy (CICS) | ✓ |  |  | 
Small-angle X-ray scattering (SAXS). | ✓ |  |  | 
Zeta potential Analysis |  | ✓ |  | ✓

## Slide 23
Techniques | Offline | Atline | Online | Inline
X-ray Diffraction (XRD) | ✓ |  |  | 
High-Performance Liquid Chromatography (HPLC) |  |  | ✓ | 
Fourier Transform Infrared Spectroscopy (FTIR) | ✓ |  | ✓ | 
PVM (Particle Vision and Measurement) |  |  |  | ✓
Photometric stereo imaging |  |  | ✓ | 

## Slide 24
Techniques | Offline | Atline | Online | Inline
Differential Scanning Calorimetry (DSC) | ✓ |  |  | 
Liquid Chromatography |  | ✓ |  | 
Optical Microscopy and Electron Microscopy | ✓ |  |  | 
pH sensors |  |  |  | ✓
Flow meters |  |  |  | ✓
Temperature probs |  |  |  | ✓
Conductivity sensors |  |  |  | ✓

## Slide 25: Resources
K. Knop and P. Kleinebudde, “PAT-tools for process control in pharmaceutical film coating applications,” International Journal of Pharmaceutics, vol. 457, no. 2, pp. 527–536, 2013, doi: 10.1016/j.ijpharm.2013.01.062.
https://drive.google.com/file/d/1qwG77msmF2oO8doUGwgtkrXdz0KD0xtk/view?usp=drive_link
M. B. Taraban, K. T. Briggs, P. Merkel, and Y. B. Yu, “Flow water proton NMR: In-line process analytical technology for continuous biomanufacturing,” Analytical Chemistry, vol. 91, no. 21, pp. 13538–13546, 2019, doi: 10.1021/acs.analchem.9b02622.
T. R. M. De Beer, C. Bodson, B. Dejaegher, B. Walczak, P. Vercruysse, A. Burggraeve, A. Lemos, L. Delattre, Y. Vander Heyden, J. P. Remon, C. Vervaet, and W. R. G. Baeyens, “Raman spectroscopy as a process analytical technology (PAT) tool for the in-line monitoring and understanding of a powder blending process,” Journal of Pharmaceutical and Biomedical Analysis, vol. 48, no. 3, pp. 772–779, 2008, doi: 10.1016/j.jpba.2008.07.023.
K. M. Prentice, A. Wallace, and C. Eakin, “Inline Protein A Mass Spectrometry for Characterization of Monoclonal Antibodies,” Analytical Chemistry, vol. 87, no. 5, pp. 2790–2796, 2015, doi: 10.1021/ac504502e.

## Slide 26
K. He, H. Cheng, W. Du, and F. Qian, “Online updating of NIR model and its industrial application via adaptive wavelength selection and local regression strategy,” Chemometrics and Intelligent Laboratory Systems, vol. 134, pp. 79–88, 2014, doi: 10.1016/j.chemolab.2014.03.007.
R. Reichert, J. Schnaidt, Z. Jusys, and R. J. Behm, “The influence of reactive side products on the electrooxidation of methanol—A combined in situ infrared spectroscopy and online mass spectrometry study,” Physical Chemistry Chemical Physics, vol. 16, pp. 13780–13799, 2014, doi: 10.1039/C4CP01229A.
D. A. Foley, E. Bez, A. Codina, K. L. Colson, M. Fey, R. Krull, D. Piroli, M. T. Zell, and B. L. Marquez, “NMR flow tube for online NMR reaction monitoring,” Analytical Chemistry, vol. 86, no. 24, pp. 12008–12013, 2014, doi: 10.1021/ac502300q.
A. Agoston, C. Otsch, J. Zhuravleva and B. Jakoby, "An IR-absorption sensor system for the determination of engine oil deterioration [automotive applications]," SENSORS, 2004 IEEE, Vienna, Austria, 2004, pp. 463-466 vol.1, doi: 10.1109/ICSENS.2004.1426200. keywords: {Sensor systems;Engines;Petroleum;Automotive applications;Electromagnetic wave absorption;Infrared spectra;Spectroscopy;Laboratories;Oxidation;Condition monitoring},
E. L. Veale, J. Irudayaraj, and A. Demirci, “An on-line approach to monitor ethanol fermentation using FTIR spectroscopy,” Biotechnology Progress, vol. 23, no. 2, pp. 494–500, 2007, doi: 10.1021/bp060306v.

## Slide 27
N. K. Brahma, W. T. Corns, P. B. Stockwell, L. Ebdon, and E. H. Evans, “At-line determination of mercury in process streams using atomic fluorescence spectrometry,” Journal of Analytical Atomic Spectrometry, vol. 12, pp. 611–616, 1997, doi: 10.1039/A608550D.
C. Hakemeyer, U. Strauss, S. Werz, G. E. Jose, F. Folque, and J. C. Menezes, “At-line NIR spectroscopy as effective PAT monitoring technique in Mab cultivations during process development and manufacturing,” Talanta, vol. 90, pp. 12–21, 2012, doi: 10.1016/j.talanta.2011.12.042.
D. S. Watson, K. R. Kerchner, S. S. Gant, J. W. Pedersen, J. B. Hamburger, A. D. Ortigosa, and T. I. Potgieter, “At-line process analytical technology (PAT) for more efficient scale up of biopharmaceutical microfiltration unit operations,” Biotechnology Progress, vol. 32, no. 1, pp. 108–115, 2016, doi: 10.1002/btpr.2193.
D. Yang and K. Frano, “Portable Raman spectroscopy for at-line characterization of carbon nanomaterials,” Spectroscopy Online, Jun. 1, 2018. [Online]. Available: https://www.spectroscopyonline.com/view/portable-raman-spectroscopy-line-characterization-carbon-nanomaterials
M. A. P. McAuliffe, G. E. O’Mahony, C. A. Blackshields, J. A. Collins, D. P. Egan, L. Kiernan, E. O’Neill, S. Lenihan, G. M. Walker, and A. M. Crean, “The use of PAT and off-line methods for monitoring of roller compacted ribbon and granule properties with a view to continuous processing,” Organic Process Research & Development, vol. 19, no. 1, pp. 158–166, 2015, doi: 10.1021/op5000013.
R. van Reis and A. L. Zydney, “Bioprocess membrane technology,” Journal of Membrane Science, vol. 297, pp. 16–50, 2007.
R. H. Perry and D. W. Green, Perry’s Chemical Engineers’ Handbook, 8th ed. New York, NY, USA: McGraw-Hill, 2008.
P. R. Cullis, S. C. Semple, and M. J. Hope, “Lipid nanoparticle formulations for nucleic acid delivery,” U.S. Patent 8,492,359, Jul. 23, 2013.

## Slide 28
THANK YOU!!!