## Slide 1
LNP Manufacturing and Process
Simulation
CL 299 presentation 5
Supervisor:
Prof. Kaustubh S. Rane Department of Chemical Engineering
Presented by:
Rhythem Soni 24110296 Aman Bola 24110032 Saket Jonwal 24110311

## Slide 2: Energy Balance
Equipment | Typical Lab Power Range
Syringe pump | 5–20 W
Magnetic stirrer | 5–15 W
Peristaltic pump | 20–60 W
TFF circulation pump | 80–120 W
Ptotal = 200 W
Energy consumption of the system is calculated using the equation:
E = P × t
E = 0.22 kWh

## Slide 3: What is in the Code?
A Python-based simulator that takes feed compositions and flow rates as input and automatically calculates every stream in the process — including TFF splits and ethanol removal.

## Slide 4: What You Input in the Code
Molar Ratios — Organic Phase Ionizable Lipid Helper Lipid Cholesterol PEG Lipid Cholesterol Ratios converted to wt% using MW of each component
Molar Ratios — Aqueous Phase mRNA Buffer Absolute concentrations set separately as mg/mL inputs
Feed Flow Rates Aqueous feed flow (mL/min) Organic feed flow (mL/min) Changing these two values changes every downstream flow automatically
Feed Concentrations mRNA conc in aqueous feed (mg/mL) Buffer salt conc (mg/mL) Total lipid conc in organic feed (mg/mL)
Process Parameters Encapsulation efficiency (fraction, e.g. 0.90) Target ethanol vol% (e.g. 8.0%) TFF Volume Reduction Ratio — VRR Diavolumes N (for C = C₀·e⁻ᴺ) LNP retention at membrane Salt sieving coefficient Sterile filter dead volume (mL) Process parameters are fixed equipment settings — not changed per run

## Slide 5: Key Equations Used in the Model
Mole Fraction → Mass Fraction wfᵢ = (xᵢ × MWᵢ) / Σ(xⱼ × MWⱼ)
Diafiltration Ethanol Removal (C = C₀ · e⁻ᴺ) C_ethanol = C₀ × exp(−N) Standard diafiltration washout equation. N = number of diavolumes. N=5 → 99.3% removal. Used in FDA submissions and industry protocols.
Dilution Buffer Calculation V_dil = V_EtOH / (target% / 100) − V_S12 Back-calculates dilution buffer volume required to reduce ethanol from post-mixer level to target vol%. Adjusts automatically for any FRR.
Buffer Salt Removal with Sieving Coefficient C_salt = C₀ × exp(−σ × N) Extension of ethanol model. σ (sieving coefficient) = fraction passing per diavolume. For 100 kDa membrane + small salts, σ ≈ 1.0.
TFF Volume Reduction Ratio
VRR = V_S13 / V_retentate

## Slide 6: Sample Output (aq = 9 mL/min, org = 3 mL/min)
Stream | Flow (mL/min) | Ethanol (vol%) | LNP Mass Flow (mg/min)
Aqueous Feed | 9.00 | — | 2.70 (mRNA)
Organic Feed | 3.00 | 98.7% | 30.00 (lipids)
Crude LNP (S12) | 12.00 | 24.7% | 32.70
Dilution Buffer | 25.02 | — | —
Diluted LNP (S13) | 37.02 | 8.0% | 32.70
DF Buffer → TFF | 37.02 | — | —
TFF Permeate | 66.64 | ~99%→0 | 1.65 (lost)
TFF Retentate | 7.40 | 0.2% | 29.28
Final Product | 7.40 | 0.2% | 29.28
Balance Error
0%
Encapsulated mRNA Recovery
89.1%
Ethanol Removed (N=5 diavolumes)
99.33%

## Slide 7: What the Simulator Outputs
Feed Streams Flow rate (mL/min) Concentration of each component (mg/mL) Mass flow of each component (mg/min)
Final Product Stream Final product flow rate (mL/min) Concentration of all components in product Mass flow of each component in final product Encapsulated mRNA mass flow and recovery %
Calculated Process Flows Dilution buffer added (auto-calculated from target ethanol %) Ethanol vol% at each stage DF buffer flow (auto-scaled from diavolumes × retentate) TFF permeate flow (auto-calculated from VRR)
Balance Verification Total mass IN vs total mass OUT Volumetric flow accounting (IN = OUT) Balance error (%) Sterile filter dead volume noted separately

## Slide 8: PAT

## Slide 9: PAT classification - INLINE
Now we have classification of PAT techniques used in LNP manufacturing.
Dynamic light scattering(DLS) measure particle size and distribution & PDI (<0.2).
Zeta potential analysis measure surface charge that indicates the stability of suspension.
Optical turbidity measurement(turbidity probes) it detects incorrect lipid mixing aggregation and wrong molecule formation.
PVM capturing image while LNPs are forming
NIR monitor composition and concentration of components in real time without sampling.

## Slide 10
UV–Vis Spectroscopy it monitors Concentration of lipids, Encapsulated drug / RNA, Particle formation kinetics and Impurities.
pH sensor at the buffer mixing for correct pH.
flow meter measure flow rate of liquid streams.
temp prob
conductivity sensor buffer dilution verification.
Pressure sensor in TFF filtration.
Raman spectroscopy

## Slide 11: Online
High-Performance Liquid Chromatography (HPLC) On-line possible via auto-samplers for drug loading, encapsulation efficiency, or degradation monitoring.
Raman spectroscopy used as a downstream analytical tool to measure how much mRNA is successfully encapsulated inside lipid nanoparticles.
Charged aerosol detectors (CAD) Used with chromatography to detect and quantify lipid components in LNP formulations that do not absorb UV light
Refractive index (RI) Measures changes in refractive index to detect lipids and polymers in LNP samples during chromatographic analysis.

## Slide 12
ultraviolet(UV) diode array Detects UV-absorbing molecules such as RNA or drugs in LNP formulations while simultaneously recording their absorption spectra
LC-MS lipid identification and impurity detection

## Slide 13: Atline
Raman spectroscopy
Zeta potential analysis
DLS
NMR lipid structure and molecular interactions
Cryo-TEM Visualize morphology and internal structure of LNPs confirm nanoparticle formation and observe structure of lipid core.

## Slide 14: Resources:
M. Mehta and T. A. Bui, “Lipid-Based Nanoparticles for Drug/Gene Delivery: An Overview of the Production Techniques and Difficulties Encountered in Their Industrial Development,” ACS Materials Au, vol. 3, no. 6, pp. 600–619, 2023, doi: 10.1021/acsmaterialsau.3c00032.
J. Auclair and A. S. Rathore, “Analysis of Lipid Nanoparticles,” LCGC North America, vol. 41, no. 6, pp. 216–219, Jun. 2023, doi: 10.56530/lcgc.na.ii3372s8.
S. Jin and E. Reverdatto, “Encapsulation of mRNA in Therapeutics Like Lipid Nanoparticles Probed by Deep-UV Resonance Raman Spectroscopy,” Analytical Chemistry, vol. 97, 2025, doi: 10.1021/acs.analchem.5c04246.
J. A. Kulkarni, D. Witzigmann, S. Chen, P. R. Cullis, and R. van der Meel, “On the formation and morphology of lipid nanoparticles containing ionizable cationic lipids and siRNA,” ACS Nano, vol. 15, no. 5, pp. 9078–9093, May 2021, doi: 10.1021/acsnano.1c03058.
https://drive.google.com/drive/folders/10AyL6bArZ2kjxkyHl5krHhYheAy40hMO?usp=drive_link
D. W. Green and M. Z. Southard, Perry’s Chemical Engineers’ Handbook, 9th ed. New York, NY, USA: McGraw-Hill Education, 2019.

## Slide 15
G. Towler and R. Sinnott, Chemical Engineering Design: Principles, Practice and Economics of Plant and Process Design, 3rd ed. Oxford, U.K.: Elsevier, 2022.
N. M. Belliveau, J. Huft, P. J. Lin, S. Chen, A. K. K. Leung, J. B. Leaver, A. W. Wild, J. B. Lee, R. J. Taylor, Y. K. Tam, C. L. Hansen, and P. R. Cullis, “Microfluidic synthesis of highly potent limit-size lipid nanoparticles for in vivo delivery of siRNA,” Molecular Therapy – Nucleic Acids, vol. 1, no. 8, p. e37, Aug. 2012, doi: 10.1038/mtna.2012.28.
R. van Reis and A. L. Zydney, “Membrane separations in biotechnology,” Current Opinion in Biotechnology, vol. 18, no. 3, pp. 208–211, Jun. 2007.

## Slide 16
THANK YOU!!!